## Slide 1
Autodesk AEC DevCamp 2012
Autodesk Revit Materials, Physical Properties and Compound Structure API Basics
Steven Mycynek Principal Engineer

## Slide 2: Outline
Material Model History
Material Properties
Dealing with Units
Working with Materials
GbXML’s role in Revit
Family Thermal Properties
Layered Assemblies
Layered Assembly Thermal Properties
A few last enhancements

## Slide 3: 1) Material Model History

## Slide 4: 2) Material Properties

## Slide 5: Materials Model History
Materials in 2011
  Inheritance model
Materials in 2012
  PropertySet model, Material subclasses obsolete
Materials in 2013
  PropertySet plus Asset model, Material subclasses removed
Why the changes?
  Extensibility for the future
    Add another asset, not derive another subclass.
  Better Element Filter support
  AIRMax compatibility

## Slide 6: 2) Material Properties

## Slide 7: Material Property Hierarchy
Material
  PropertySetElement – generic parameter bag
    StructuralAsset – discoverable props, new in 2013
  PropertySetElement – generic parameter bag
    ThermalAsset – discoverable props, new in 2013
  API documentation
    Material.ThermalAssetId
    Material.StructuralAssetId

## Slide 8: Asset types and properties
  ThermalAsset
    ThermalMaterialType
      Solid
      Liquid
      Glass
      Undefined
  StructuralAsset
    StructuralAssetClass
      Undefined
      Basic
      Generic
      Metal
      Concrete
      Wood
      Liquid
      Gas
      Plastic
Not all properties in each asset apply to all types, e.g. “LiquidViscosity”
Watch out for InapplicableDataException.
See documentation for details.

## Slide 9: MaterialClass property – new in 2013
A simple, top-level string property on Material
Useful for casual categorization
Already filled out for standard materials
Users asked for it with 2012.

## Slide 10: 3) Units

## Slide 11: Working with Units
  Who’s had confusion and frustration here ? 
  Revit Internal Units
    Unless documented otherwise…
      Lengths in decimal feet
      All other units in metric
      Compound units can be tricky
  Revit UI units – any number of common metric or imperial units
    Document.ProjectUnit[].FormatOptions
  Converting units
    Helper method in ExporterIFCUtils
  Code walkthrough – units sample
    UnitUtility.cs

## Slide 12: UnitUtility.cs sample code
  Helper Methods in today’s sample code
    SystemToDisplayUnits
      A wrapper around an IFC API method
      Double
      XYZ
    DisplayUnitsToSystem
      Had to do a little extra math
    FormatValue
      Shows in both API/System units and current display units.

## Slide 13: 4) Working with Materials

## Slide 14: Materials UI

## Slide 15: Creating a material – General Guidelines
Materials are complicated and have a lot of data
  No longer just a texture map.
Have a plan when creating a new one
  Do you want a totally new material?
  Maybe a material very similar to an existing one?
  What in particular is “new” about this new one?
Organize your code well

## Slide 16: Creating a material
Creation though duplication
  Duplicate the Material
    Material.Duplicate()
    Just the top-level items – a “shallow copy”
  Duplicate Assets
    ThermalAsset and StructuralAsset Copy() method
    Setting with new data is somewhat optional
  Duplicate PropertySetElements
    PropertySetElement.Duplicate()
    New elements to be saved in the Revit document
  Set PropertySetElements to material
    Combine everything from above into one DB.Material

## Slide 17: Creating a material
Creation from scratch
  Create a new material with Material.Create()
  Create assets
    ThermalAsset constructor
    StructuralAsset constructor
  Create PropertySetElements
    PropertySetElement.Create
      Requires assets from (2) as input
  Set PropertySetElements to Material
    Material.StructuralAssetId
    Material.ThermalAssetId

## Slide 18: Demo: Creating a material through duplication

## Slide 19: Demo: Creating a new material from scratch

## Slide 20: 5) GBXML in Revit

## Slide 21: GBXML
What is it?
Who uses it outside of Revit?
Where is it used in Revit?
Understanding the format

## Slide 22: GBXML –What is it?
Open source energy data format
http://www.gbxml.org/currentschema.php

## Slide 23: GBXML –Who uses it outside of Revit?
DOE-2 (doe2.com)
Green Building Studio (gbs.autodesk.com)
Bentley
Carmel Software
Trane
Carrier

## Slide 24: GBXML –Where is it used in Revit?
Family thermal properties
  Doors
  Windows
  Curtain Panels
Constructions Overrides
  As an alternative to layer-calculated properties
  Use a known agreed-on GBXML data set instead
General Export
  Entire thermal model of building.

## Slide 25: Understanding the GBXML format.
Constructions.xml -- It’s in your Revit.exe folder.
100% GBXML
A few key elements
  Construction – a wall, door, ceiling, or other type
  Material – a physical medium with thermal properties.
  WindowType – a thermal description of a window

## Slide 26: Constructions.xml - Windows
  WindowType – a complete window assembly
    Name and Id
    U-value
    SolarHeatGainCoefficient (only for an angle of 0)
    Visual Light Transmittance

## Slide 27: Constructions.xml - Doors
  Construction– a complete window assembly
    Name and Id
    surfaceType =“NonSlidingDoor”
    U-value

## Slide 28: Where does contructions.xml end up in the API?
  Stay tuned…

## Slide 29: 6) Family Thermal Properties

## Slide 30: FamilyThermalProperties class
  Class basics:
    A thermal property class for families
    No constructor
    Static Find() method to get by Id*
    All Properties are read-only
    Get/Set method on FamilySymbol
  What can you do?
    Read thermal from families.
    *Find thermal data in constructions.xml
    Reassign thermal data from constructions.xml to families.

## Slide 31: Window Family thermal properties – Exposed!

## Slide 32: Demo – Family Thermal Properties
  API Macro to view and set family thermal properties.

## Slide 33: Not all thermal properties are GBXML based
  Stay tuned…

## Slide 34: 7) Layered Assemblies

## Slide 35: Layered Assemblies
What element types are layered?
  WallType
  FloorType
  RoofType
  CeilingType
  BuildingPadType

## Slide 36: A bit about the layers API
Much of the API for compound structure and layers is not new to 2013
  Quick review of API
    CompoundStructure
    CompoundStructureLayer
    WallType.Get/SetCompoundStructure()
    CompoundStructure.SetLayers()

## Slide 37: Wall Layers UI
Function
Material
Thickness
Structural?
  New 2013

## Slide 38: CompoundStructure class in detail
A property of HostObjAttributes
  WallType
  FloorType
  CeilingType
  …
Not an instance property.
Must be explicit set via SetCompoundStructure()
StructrualLayerIndex – new in 2013

## Slide 39: CompoundStructureLayer class in detail
Most important properties
  Width
  MaterialId
    Much more important now that materials have more analytical data.
  Function
    Insulation, membrane, etc…

## Slide 40: 8) Layered Assembly Thermal Properties

## Slide 41: ThermalProperties class
  Class basics
    A thermal property class for layered assembly types
      New in 2013
    No constructor or class factory method
    Some read-write properties, some read-only.
  What can you do?
    Read thermal data from layered assembly types.
    Adjust certain properties.
      Absorptance
      Roughness
    View driven properties
      U-Value
      R-Value
      Thermal Mass

## Slide 42: ThermalProperties - Driven
  How are driven properties generated?
      From the ThermalAsset data in the materials in the layers of the assembly.
      Some older materials may not have thermal assets.
      Adjust your layers and materials to see overall assembly properties change.

## Slide 43: WallType property hierarchy
WallType
  ThermalProperties
    Writeable (Absorptance, Roughness)
    Driven by CompoundStructure (ThermalMass, Resistance, HTC)
  CompoundStructure
      CompoundStructureLayer
        Material
          PropertySetElement
            StructuralAsset
          PropertySetElement
            ThermalAsset
      CompoundStructureLayer
        …..

## Slide 44: WallType thermal properties – Exposed!

## Slide 45: How do driven thermal properties change?
The inherent thermal nature of a material.
The amount of that material.
We can adjust both in the UI or API and observe the projected thermal results.

## Slide 46: Demo – layered assembly thermal properties

## Slide 47: Demo: Change a layer material
Note the overall thermal properties of an assembly.
Change a material.
  Note our two demo materials
  Concrete_standard
  Concrete_highConductivity
Note the result.

## Slide 48: Demo: Increase a layer width
Note the overall thermal properties of a wall assembly.
Change a width.
Note the result.

## Slide 49: Demo: Wall analysis
In the API, I can…
  Query layer widths
  Query with layers are insulation
  Query overall R-Value
  Edit a wall’s layer widths
Let’s put all of these together!

## Slide 50: Demo: Wall analysis
Visualize how total R-Values change
  …by adjusting small pieces of a design.
Reset the design to its original configuration when done.

## Slide 51: Demo: Wall analysis
Select a sample wall
Make several trial adjustments insulation widths
Record and display results

## Slide 52: 9) A few last things

## Slide 53: Structural Material Id
(FamilyInstance.StructuralMaterialId)

## Slide 54: Construction overrides
Analyze->H&C Loads -> Building Construction
  Demo

## Slide 55: Thank you
steven.mycynek@autodesk.com

## Slide 56
Autodesk, AutoCAD, Alias, Revit, Autodesk Inventor, Inventor, Maya, Mudbox, and 3ds Max are registered trademarks or trademarks of Autodesk, Inc., and/or its subsidiaries and/or affiliates in the USA and/or other countries. Academy Award and Oscar are registered trademarks of the Academy of Motion Picture Arts and Sciences. mental ray is a registered trademark of mental images GmbH licensed for use by Autodesk, Inc. All other brand names, product names, or trademarks belong to their respective holders. Autodesk reserves the right to alter product and services offerings, and specifications and pricing at any time without notice, and is not responsible for typographical or graphical errors that may appear in this document.
© 2012 Autodesk, Inc. All rights reserved.